Introduction
Introduction
Chapter 1
CSI 2121, Winter 2000
Lecture Notes Written by Mario Marchand
http://www.site.uottawa.ca/~marchand/

---
The Bottom-up Approach
The Bottom-up Approach
We can study computer architectures by starting with the basic building blocks
  - Transistors and logic gates
To build more complex circuits
  - Flip-flops, registers, multiplexors, decoders, adders, ...
From which we can build computer components
  - Memory, processor, I/O controllers…
- Which are used to build a computer system
- This was the approach taken in your first course CSI 2121: computer architecture I

---
The Top-bottom Approach
The Top-bottom Approach
- In this course we will study computer architectures from the programmer’s view
- We study the actions that the processor needs to do to execute tasks written in high level languages (HLL) like C/C++, Pascal, …
- But to accomplish this we need to:
  - Learn the set of basic actions that the processor can perform: its instruction set
  - Learn how a HLL compiler decomposes HLL command into processor instructions

---
The Top-bottom Approach (Ctn.)
The Top-bottom Approach (Ctn.)
We can learn the basic instruction set of a processor either
  - At the machine language level
    - But reading individual bits is tedious for humans
  - At the assembly language level
    - This is the symbolic equivalent of machine language (understandable by humans)
- Hence we will learn how to program a processor in assembly language to perform tasks that are normally written in a HLL
  - We will learn what is going on beneath the HLL interface

---
Levels and Languages
Levels and Languages
High-level
language
program
Assembly
language
program
Machine
language
program
Compiler
Assembler
- The compiler translates each HLL statement into one or more assembly language instructions
- The assembler translate each assembly language instruction into one machine language instruction
  - Each processor instruction can be written either in machine language form or assembly language form
  - Example, for the Intel Pentium:
    - MOV al, 5 ;Assembly language
    - 10110000 00000111 ;Machine language
Hence we will use assembly language

---
Assembly Language Today
Assembly Language Today
- A program written directly in assembly language has the potential to be smaller and to run faster than a HLL program
- But it takes too long to write a large program in assembly language
  - Only time-critical procedures are written in assembly language (for speed optimization)
Assembly language are often used in embedded system programs stored in PROM chips
  - Computer cartridge games, micro controllers, …
Remember: you will learn assembly language to learn how high-level language code gets translated into machine language
  - i.e. to learn the details hidden in HLL code

---
The Platform We Will Use
The Platform We Will Use
Assembly language and machine language are processor specific
  - We will write code for Intel’s x86 (x>=3)
The assembler places its machine code into an object file which is OS specific
  - Our code will run (only) on Windows 95/98/NT
    - And it will crash on DOS
  - Our programs will be Win32 console applications
    - These are programs for which all I/O operations are character-based
    - They run into a MS-DOS box but they are not DOS programs (they do not use DOS calls)

---
The Intel X86 Family
The Intel X86 Family
. . .
Pentium
80486
80386
80286
8086
The instruction set of the x86 is backward compatible with any one of its predecessors
  - New additional instructions are introduced with each new processor

---
Registers
Registers
Registers are the fastest memories
  - Located directly on the processor
  - Manipulated directly by processor instructions
- The registers for the 8086 and 80286 are only 16-bit wide
- Most of these registers have been extended to 32 bits for the 80386 and higher processors
  - But very few extra registers have been added
The Pentium has very few registers
  - Only 8 registers are available to the programmer (apart from the segment and FPU registers)

---
General Purpose Registers
General Purpose Registers
0
31
15
0
BH
BL
EAX
AH
AL
EBX
BX
AX
7
0
DH
DL
EDX
ECX
CH
CL
DX
CX
- Used by the programmer for arithmetic and data movement
- AX is the least significant part of EAX and can be accessed independently (by its name)
- AH and AL can also be accessed independently
- This is also true for EBX, ECX and EDX
- Only the 16-bit part are present in the 8086 and 286

---
Index Registers
Index Registers
0
31
SP
ESI
SI
ESP
15
0
BP
EBP
EDI
DI
- The least significant half can be accessed independently (since it has a name)
- Only the lower 16-bit was present in 8086 and 286
- Used often to carry the offset part of the logical address (more on that later)
  - ESI and EDI for the data segment
  - ESP and EBP for the stack segment

---
The Instruction Pointer EIP
The Instruction Pointer EIP
15
0
31
EIP
IP
EIP always contains the offset address of the instruction to be executed next
  - This is the program counter for the x86
  - The offset address is 32-bit wide when the processor runs in 32-bit mode (ie: for 32-bit segments)
  - It is 16-bit wide in 16-bit mode
Only the lower 16-bit was present in the 8086 and 80286 (called IP)

---
EFLAGS and Condition Codes
EFLAGS and Condition Codes
31
15
0
EFLAGS
FLAGS
- The condition codes of the processor are stored in the EFLAGS register
- They consist of individual bits indicating either:
  - The mode of operation of the CPU. Ex:
      - DF: indicates if arrays are processed in the direction of increasing addresses
  - The outcome of an arithmetic operation. Ex:
      - ZF: indicates if the result is zero
      - SF: indicates if the result is negative
      - CF: indicates if there is an unsigned overflow
      - OF: indicates if there is a signed overflow

---
Segment Registers
Segment Registers
Each program is subdivided into logical parts called SEGMENTS
  - Code segment (CS)
  - Stack segment (SS)
  - Data segments (DS, ES, FS, and GS)
- Segment registers hold the “base address” of these program segments
- Segment registers are 16-bit wide
CS
SS
DS
ES
FS
GS

---
Logical and Physical Addresses
Logical and Physical Addresses
- Addresses specify the location of instructions and data
- Addresses that specify an absolute location in main memory are physical addresses
  - They appear on the address bus
Addresses that specify a location relative to a point in the program are logical (or virtual) addresses
  - They are addresses used in the code and are independent of the structure of main memory
Each logical address for the x86 consist of 2 parts:
  - A segment number used to specify a (logical) part of the program
  - A offset number used specify a location relative to the beginning of the segment

---
Address Translation and Running Modes
Address Translation and Running Modes
- The translation from logical to physical addresses is done at run time
- The way in which this address translation is done depends on the running mode of the x86
- Two different running modes exist for the x86:
  - Real mode (supported by every x86)
  - Protected mode (all x86 except the 8086)

---
Address Translation in Real Mode
Address Translation in Real Mode
The 16-bit segment number (contained in a segment register) is first multiplied by 16
  - Ex: if CS contains 15A6h (in hexadecimal), we obtain the 20-bit value 15A60h
Then we add to this a 16-bit offset number to obtain a 20-bit physical address
  - Ex: if the offset number is 0012h, we obtain the physical address 15A60h + 0012h = 15A72h

---
Characteristics of (Archaic) Real Mode
Characteristics of (Archaic) Real Mode
- Can address only up to 1MB of physical memory
- Does not support multitasking
  - Only 1 process at a time is active
- No protection is provided: a program can write anywhere (and corrupt the operating system)
- The 8086 runs only in this mode
- DOS is a real-mode operating system
- Our programs will not run in this archaic mode
  - They will run in protected mode which does not suffer any of these limitations

---
Address Translation in Protected Mode
Address Translation in Protected Mode
- The logical/virtual address of a referenced word is given by a pair of numbers (segment, offset)
- The segment number is contained in a segment register and is used to select (or index) an entry in a segment table (called a descriptor table)
  - Hence, a segment resister is also called a selector
- The selected entry (the descriptor) contains the base address and length of the referenced segment
- The 32-bit base address is added to the 32-bit offset to form a 32-bit linear address (P1,P2,D)
  - P1 indexes a directory page table (in memory) to obtain the base address of a second page table which is indexed by P2 to give the physical address of the referenced word

---
Intel 386  Address  Translation
Intel 386
Address
Translation
P1
P2
D

---
The FLAT Memory Model
The FLAT Memory Model
The segmentation part is “effectively disabled” when the base address of each segment descriptor is the same
  - Each selector then points to the same segment so that code, data, and stack share the same segment
  - Protection bits (read-only, read-write) in each descriptor can still be used
  - Done by Windows 95/98/NT, Linux, FreeBSD…
The offset part of the logical address is then equivalent to the linear address (P1,P2,D).
  - Only the offset part of the logical address is used to specify the location of a referenced word
  - The address space is then said to be FLAT
  - All our programs will use the FLAT memory model

---
Memory Units for the x86
Memory Units for the x86
The smallest addressable unit is the BYTE
  - 1 byte = 8 bits
- For the x86, the following units are used
  - 1 word = 2 bytes
  - 1 double word = 2 words (= 32 bits)
  - 1 quad word = 2 double words

---
Data Representation
Data Representation
- To obtain the value contained in a block of memory we need to choose an interpretation
- Ex: memory content 0100 0001 can either represent:
  - The number
  - Or the ASCII code of character “A”
- Only the programmer can provide a interpretation
size 12{2 rSup { size 8{6} } +1="65"} {}

---
Character Representation
Character Representation
- Each character is represented by a 7-bit code called the ASCII code
- ASCII codes run from 00h to 7Fh (h = hexadecimal)
  - Only codes from 20h to 7Eh represent printable characters. The rest are control codes (used for printing, transmission…).
An extended character set is obtained by setting the most significant bit (MSB) to 1 (codes 80h to FFh) so that each character is stored in 1 byte
  - This part of the code depends on the OS used
    - For Windows: we find accentuated characters, Greek symbols and some graphic characters

---
The ASCII Character Set
The ASCII Character Set
CR = “carriage return” (Windows: move to beginning of line)
LF = “line feed” (Windows: move directly one line below)
SPC = “blank space”

---
Text Files
Text Files
- These are files containing only ASCII characters
- But different conventions are used for indicating an “end-of line”
  - Windows: <CR>+<LF>
  - UNIX: <LF>
  - MAC: <CR>
- This is at the origin of many problems encountered during transfers of text files from one system to another

---
Number Systems
Number Systems
- A written number is meaningful only with respect to a base
- To tell the assembler which base we use:
  - Hexadecimal 25 is written as 25h
  - Octal 25 is written as 25o or 25q
  - Binary 1010 is written as 1010b
  - Decimal 1010 is written as 1010 or 1010d
You already know how to convert from one base to another (if not, review 1st year class notes)

---
Integer Representations
Integer Representations
- Two different representations exists for integers
- The signed representation: in that case the most significant bit (MSB) represents the sign
  - Positive number (or zero) if MSB = 0
  - Negative number if MSB = 1
- The unsigned representation: in that case all the bits are used to represent a magnitude
  - It is thus always a positive number or zero

---
Twos Complement Notation
Twos Complement Notation
- Used to represent negative numbers in the signed representation
- The twos complement of a number X, denoted by NEG(X), is obtained by complementing all its bits and adding +1
- Hence, by definition: NEG(X) = NOT(X) + 1
  Ex: NEG(10) = NOT(10) + 1
  = NOT(0000 1010b) + 1
  = (1111 0101b) + 1 = 1111 0110b
  = NEG(10) = -10
We always have: X + NEG(X) = 0
  - i.e. NEG(X) is the additive inverse of X
To perform the difference X - Y:
  - the machine executes the addition X + NEG(Y)

---
Twos Complement Notation (Cont.)
Twos Complement Notation (Cont.)
- Note that we have NEG(10) = 1111 0110b when we use 1 byte of storage
- But NEG(10) = 1111 1111 1111 0110b when we use 1 word of storage
- Exercise: compute the twos complement of the following numbers and mention if there is an overflow (i.e. when the given storage is not large enough to hold the result)
  - A) 16 on 1 byte of storage
  - B) -16 on 1 byte of storage
  - C) -128 on 1 byte of storage
  - D) -128 on 1 word of storage
  - E) 0 on 1 word of storage

---
Maximum and Minimum Values
Maximum and Minimum Values
The MSB of a signed integer is used for its sign
  - fewer bits are left for its magnitude
Ex: for a signed byte
  - smallest positive = 0000 0000b
  - largest positive = 0111 1111b = 127
  - largest negative = -1 = 1111 1111b
  - smallest negative = 1000 0000b = -128
Exercise: give the smallest and largest positive and negative values for
  - A) a signed word
  - B) a signed double word

---
Signed and Unsigned Interpretation
Signed and Unsigned Interpretation
- To obtain the value of a integer in memory we need to chose an interpretation
- Ex: a byte of memory containing 1111 1111 can represent either one of these numbers:
  - -1 if a signed interpretation is used
  - 255 if an unsigned interpretation is used
- Only the programmer can provide an interpretation of the content of memory